Fault tolerant filter implemented using N-modular redundancy

Project – Fault tolerant systems

Miloš Arbanas

# Introduction
The goal of the project is described in following section.

# Methodology
First, the ordinary filter should be developed, then fault modeling should be added, and, at the end, redundancy to detect and handle faults.
## Developing VHDL model of a generic order FIR filter
This is fairly simple and only few notes will be taken.
Data representation used for calculations is Fixed Point Q1.23.
Both additions and multiplications are done using FPGA DSPs. In Xilinx FPGA these are 48 bit DSPs.
Addition: we should be aware of the possibility for Overflow to happen. Like on the picture below:
Simplest way to handle this situation is to saturate output of a adder.

Here is the picture with saturation:

Multiplication:
All of the numbers are less than one, so there should be no problems with this.
Multiplying 2 x Q1.23 numbers gives Q2.46 number, and than one should get last bit from Whole part and first 23 bits from decimal part. Like shown in picture:

## Fault modeling
In order to test fault tolerant design, there is a need of inducing artificial faults into the system.

From this picture we can see that outputs of a Multiplication component, Adder and Register should be able to emulate Faults.
So normal components should have additional inputs that enable generating fault instead of providing calculated value.
1
First idea is to add:
3
- fault_enable
- fault value
2
And then when the fault is needed one just modify those inputs.
There are 10 MAC modules in the filter, and each module can have 3 different places where the fault might occur. So there are 30 different places combined.
So we can name all of the faults as such:
fault (x, y) => fault at MAC(x).fault(y) where “x” ranges from 1 to 10 and “y” ranges from 1 to 3.
If we want to model fault that happens on MAC 3, multiplication block, then we set MAC(3) mult_fault_enable to “1” and mult_fault_value to some Q1.23 number.