1
2
3
Fault tolerant filter implemented using N-modular redundancy

Project – Fault tolerant systems

Miloš Arbanas

# Introduction
The goal of the project is described in following section.

# Methodology
First, the ordinary filter should be developed, then fault modeling should be added, and, at the end, redundancy to detect and handle faults.
## Developing VHDL model of a generic order FIR filter
This is fairly simple and only few notes will be taken.
Data representation used for calculations is Fixed Point Q1.23.
Both additions and multiplications are done using FPGA DSPs. In Xilinx FPGA these are 48 bit DSPs.
Addition: we should be aware of the possibility for Overflow to happen. Like on the picture below:
Simplest way to handle this situation is to saturate output of a adder.

Here is the picture with saturation:

Multiplication:
All of the numbers are less than one, so there should be no problems.
Multiplying 2 x Q1.23 numbers gives Q2.46 number, and than one should get last bit from Whole part and first 23 bits from decimal part. Like shown in picture:

## Fault modeling
In order to test fault tolerant design, there is a need of inducing artificial faults into the system.

From this picture we can see that outputs of a Multiplication component, Adder and Register should be able to emulate Faults.
So normal components should have additional inputs that enable injecting of the fault instead of providing the calculated value.
First idea, for behavioral fault modeling, is to add input that will be forced to the output of the modules.
This faults emulates error in calculation.
Another idea is to try to emulate Structural fault modeling. Although we don’t have control of the system at logic level, we can emulate that by inducing fault on behavioral level that resembles faults that commonly happen on structural level.
We can either flip some bit (modeling “soft”, transient, faults that mostly environment causes).
Or we can model Stuck-At Fault by holding some bit to be always “1” (SA1) or “0” (SA0) which commonly represents faulty silicon (most frequently transistors) and it is probably permanent fault.
In order to work at the behavioral level, the new component Fault injection module will be introduced. Outputs of adder, multiplier and register will be passed through this module.
There are 10 MAC modules in the filter, and each module can have 3 different places where the fault might occur. So there are 30 different places combined.
### Fault injection module
This module changes data in order to induce a fault of different types. Fault value gives the input vector that is used and changes input signal as described:
1. behavioral fault	- output is equal to fault value
2. flip bit fault	- flips bits where fault value is “1”
3. SA1	- sets bits to “1” where fault value is “1”
4. SA0	- sets bits to “0” where fault value is “1”
Fault type is chosen with Fault type select input, by indexing fault type shown above.
Final component for fault injection is shown above and whole MAC might look something like this: