Fault tolerant filter implemented using N-modular redundancy

Project – Fault tolerant systems

Miloš Arbanas

# Introduction
The goal of the project is described in following section.

# Methodology
First, the ordinary filter should be developed, then fault modeling should be added, and at the end, redundancy to detect and handle faults.
## Developing VHDL model of a generic order FIR filter
This is fairly simple and only few notes will be taken.
Data representation used for calculations is Fixed Point Q1.23.
Both additions and multiplications are done using FPGA DSPs. In Xilinx FPGA these are 48 bit DSPs.
Addition: we should be aware of the possibility for Overflow to happen. Like on the picture below:
Simplest way to handle this situation is to saturate output of a adder.

Here is the picture with saturation: